## Slide 1: Fire extinguisher training

## Slide 2: Objectives
Understand the combustion process and different fire classes.
Understand fire extinguishers types, operating procedures, capabilities and limitations.
Understand basic firefighting concepts:
  P.A.S.S.
Fire extinguisher training
Notes: BRIEFLY REVIEW OBJECTIVES.

## Slide 3: The combustion process—The fire tetrahedron
Fire extinguisher training
Notes: For a fire to occur, you need these four ingredients in specific proportions.

## Slide 4: Fire classes
Fire extinguisher training
A Trash, wood, paper
C Electrical equipment
B Liquids and grease
Wood.
Cloth.
Paper.
Rubber.
Many plastics.
Gasoline.
Oil.
Grease.
Tar.
Oil-based paint.
Lacquer.
Flammable gasses.
Energized electrical equipment.
Notes: DESCRIBE THE THREE FIRE CLASSES
TO DECIDE IF EXTINGUISHER IS APPROPRIATE, MATCH SYMBOL TO TYPE OF FIRE BEING ENCOUNTERED.

## Slide 5: Fire extinguisher anatomy
Fire extinguisher training
Discharge hose
Discharge nozzle
Discharge orifice
Body
Data plate
Carrying Handle
Pressure gauge
(not found on CO2 extinguishers)
Discharge lever
Discharge locking pin
and seal
Notes: POINT OUT DIFFERENT COMPONENTS OF PORTABLE FIRE EXTINGUISHER.
POINT OUT THAT CO2 EXTINGUISHER IS UNIQUE IN THAT IT DOES NOT HAVE PRESSURE GAUGE.

## Slide 6
Fire extinguisher training
Fire class
Effective extinguisher types
Pressurized water
Multipurpose dry chemical
Multipurpose dry chemical
Carbon dioxide
Multipurpose dry chemical
Carbon dioxide
Trash, wood, paper
Liquids and grease
Electrical
equipment
Notes: ASK “WHAT TYPES OF EXTINGUISHERS ARE BEST SUITED ON WHICH FIRE CLASSES?”

## Slide 7: Fire extinguisher types
Fire extinguisher training
Pressurized water
For class “A” fires only.
Discharges 2.5 gal. water at 150 to 175 psi (up to 1 minute discharge time).
Has pressure gauge to allow visual capacity check.
Has a 30 to 40 ft. maximum effective range.
Can be started and stopped as necessary.
Extinguishes by cooling burning material below the ignition point.

## Slide 8: Fire extinguisher types
Fire extinguisher training
Carbon dioxide (CO2)
For class “B” or “C” fires.
Discharges 2.5 to 100 lb. of CO2 gas at 150-200 psi (8-30 seconds discharge time).
Has no pressure gauge--capacity verified by weight.
Has a 3 to 8 ft. maximum effective range.
Extinguishes by smothering burning materials.
Effectiveness decreases as temperature of burning material increases.

## Slide 9: Fire extinguisher types
Fire extinguisher training
Multipurpose dry chemical
For class “A”, “B” or “C” fires.
Discharges 2.5 to 20 lb. dry chemical (ammonium phosphate) pressurized to 50-200 psi by nitrogen gas (8-25 seconds discharge time).
Has pressure gauge to allow visual capacity check.
Has a 5 to 20 ft. maximum effective range.
Extinguishes by smothering burning materials.
Notes: THIS IS THE MOST COMMON TYPE OF FIRE EXTINGUISHER IN OUR FACILITIES.

## Slide 10
Fire extinguisher training
Extinguisher type
Works by
Cooling and smothering
Cooling and smothering
Smothering
Pressurize water
Carbon dioxide
Multipurpose dry chemical
Effective against
Notes: BRIEFLY REVIEW EACH EXTINGUISHER TYPE, STRENGTHS, WEAKNESSES.

## Slide 11: Firefighting decision criteria
Know department emergency procedures and evacuation routes.
Know locations of extinguishers in your area and how to use them.
Always notify operator or management regardless of fire size.
Avoid smoky conditions.
Ensure area is evacuated.
Fire extinguisher training
Notes: ASK “HOW DO I DECIDE TO FIGHT THE FIRE OR EVACUATE?”
IF ONE OR MORE OF THE ABOVE CRITERIA AREN’T MET, GET OUT!

## Slide 12: Firefighting decision criteria
Don’t attempt to fight unless:
  Alarm is sounded.
  Fire is small and contained.
  You have safe egress route (can be reached without exposure to fire).
  Available extinguishers are rated for size and type of fire.
If in doubt, evacuate!
Fire extinguisher training
Notes: IF YOU DO USE AN EXTINGUISHER, PLACE IT OUT OF SERVICE AND NOTIFY THE APPROPRIATE PERSON(S) SO IT CAN BE RECHARGED OR REPLACED.

## Slide 13: Summary
Combustion process.
Class “A,” “B,” “C” fires.
Types of portable fire extinguishers:
  Operating procedures.
  Capabilities and limitations.
Basic firefighting concepts:
  P.A.S.S.
Fire extinguisher training
Notes: BRIEFLY REVIEW COMBUSTION PROCESS, FIRE CLASSES, TYPES OF EXTINGUISHERS, AND THEIR LIMITATIONS
REVIEW “R.A.C.E”, “P.A.S.S.” ACRONYMS.
ASK FOR QUESTIONS.
REMIND STUDENTS TO SIGN ROSTER.

## Slide 14: QUESTIONS?